## Slide 1: Designing a Digital Computer for experimentation
Jim Brakefield
Notes: An FPGA contemplating it’s mind

## Slide 2: Introduction
Why? Computer architecture is in my DNA
Moving on from the 2016 talk:
  DIY soft-core uP Microprocessor design using an FPGA “made simple”
Goals
  My career was in real-time embedded, code size and deterministic run time mattered
Design process
Progress
Ahead
FPGA slides from previous presentation
  Which included a 24-bit RISC ISA implementation
Notes: Slides and other files posted to github.jimbrake/troc16_16

## Slide 3: Goals
Generality: create an RTL (VHDL) template
Efficiency: Register file with single cycle execution
Code density
  Variable length instructions: 16, 24 & 32-bits
  Variable length immediate values: 5, 8, 16, …
Generality again:
  Four data sizes: 8, 16, 24 & 32-bits for example
  Four data types: unsigned, signed, float, experimental
  Adaptable to non-power of two word sizes
  With restrictions*, capable of high performance
Out of the box thinking only
Notes: *Main restriction is to force 16 or 32 bit instruction alignment by using longer than necessary immediate values or inserting align op-code

## Slide 4: The Adventure Begins
Monitored usenet.comp.arch & interacted
  Refined my goals, learned the fine points of high performance architecture
  Posted my “mantra” to usenet March 3, 2015
  available along with slide deck at meeting webpage
  Some ideas came from Mitch Alsup’s My 66000
  www.linkedin.com/in/mitch-alsup-8691537/
Considered both stack and RISC architectures
  Stack ISAs have shorter instructions
  RISC ISAs have greater generality of register use
  Had difficulty devising a complete 16-bit stack ISA
  Decided to use register tag bits to imply instruction variant (e.g. data type) to save some op-code space
Early on decided on register field immediate
  Yield's 12-bit immediate on 24-bit instructions (+ one byte)
Notes: Early on decided on 5-bit register file addresses, e.g. 32 registers.

## Slide 5: The Adventure Continued
Initially went for 24 & 32-bit instructions
Over half of the op-code space unused!
Enough for a useful set of 16-bit instructions
  Only two register fields
  Limited to 32 instructions
  24 & 32-bit instructions have 25% unused op-code space, enough to hold 40 & 48-bit instructions
Unique: residue register to capture overflow
  As a distinct register, can be updated separately
A simple small ISA is a good place to start
  Can add longer instructions later
Notes: There is an issue with PC as general purpose register. It is said to conflict with high performance. Residue register to capture carry, overflow, upper half of multiply and remainder of divide. No status register, residue register can be used like any other register.

## Slide 6: Instruction formats
16-bit op-code specifies N versus R
  rrrrr ddddd xxxxx1
  nnnnn ddddd xxxxx1
24-bit has immediate enable bit
  rrrrr 0 xx sssss ddddd xxxx10
  nnnnn 1 xx sssss ddddd xxxx10
32-bit has additional op-code field
  ttttt xxx rrrrr 0 xx sssss ddddd xxxx00
  nnnnn xxx rrrrr 1 xx sssss ddddd xxxx00
Notes: Little endian dominates, so am using it. Op-code starts at the instruction LSB. R, S, T & D are register address fields. X’s are op-code bits. Register address field locations do not vary among various size instructions.

## Slide 7: Variable length immediate formats
N or I field is five bits
For troc16_16hwa if N=“10000” then the next 16-bits is the immediate, otherwise the values can be from -15 to +15.
For 24 & 32-bit instructions there are several format choices.
  Allocating four bits and the next byte eight bits allows a 12-bit signed immediate. The LS bit does the selection. This leaves four codes to indicate the size of the following immediate or a value from -4 to 7.
  Other allocations are possible
Notes: 24 & 32-bit instruction immediate formats using an addition byte 12-bit format: nnnnnnnn nnnn1, immediate size: 10ss0, -4…-1: 11nn0 or 0…7: 0nnn0

## Slide 8: Data formats
Unsigned is the usual binary
Signed can be either two’s complement or sign and magnitude with sign at the least significant end
Floats can use zero extension if both the exponent and the mantissa can be zero extended. Implies exponent and mantissa signs in the middle with exponent first.
Of the proposed floating-point formats, one typically converts between memory format and register format during memory load and store. Tag bits provided for additional exponent and mantissa bits.
Other possible formats appear to require greater logic
Notes: The consensus is that 2’s complement works better than sign & magnitude. Float format: exponent bits, exponent sign, mantissa sign, mantissa; zero extended on both ends on load, truncated on store?

## Slide 9: Example 16-bit data formats
Unsigned, has type code of zero
  0000 nnnn nnnn nnnn nnnn register format
Sign & magnitude or 2’s complement, has type code of one
  0100 nnnn nnnn nnnn nnns sign could be at either end
Simple float arranged to support zero extension
  1000 eeee sS1.mm mmmm mmmm exponent, sign & mantissa sign
Alt-754 supports gradual underflow & overflow
  eeee sS1.mm mmmm mmmm memory format
  0000 sS1.mm mm10 0000 underflow, uses # trailing zeros
  1111 sS1.mm mm10 0000 underflow, uses # trailing zeros
  11ee eeee sS1.mm mmmm mmmm register format, E adjusted
Notes: Advantage of zero extension is that it applies to all shown formats. Alt-754 underflow and overflow uses number of trailing zeros in memory format to adjust exponent. One exponent tag bit needed. 2nd tag bit for Euclidian distance computation. Consensus for exponent is off-set binary (can use sign extension).

## Slide 10: The initial implementation TROC16_16min
Tagged, Register Oriented Computer, 16+ bit instructions, 16-bit data (no tags on min variant)
32-bit memory: both an instruction and the 16-bit immediate, if needed
Two port register file
Great LUT counts! multiply instruction included
  LUTs LUTram DFF BRAM DSP clock
  16 50 0.5 1 13.6ns
  16 50 0.5 1 13.3ns area optimize
  355 144 66 0.5 1 9.7ns Fmax optimize
  Combinatorial divide adds ~400LUTs & 30ns
Notes: Targeted AMD/Xilinx Vivado 24.2, Spartan-7, Real Digital Boolean Board. FPGA has 6 input LUTs. TROC16_16min: Unsigned 16-bit data only. Three instruction loop runs, no other test bench.

## Slide 11: 16-bit instructions
INN, OUTN input/output to port N or M(N)
JSRN, BRZN, BRNZN, BRPN, BRMN control instructions (PC+N)
MOV move register: R => D
ADD,SUB,MUL,DIV,CMP,AND,OR,XOR basic arithmetic: R op D => D
ADDI,SUBI,MULI,DIVI,CMPI,ANDI,ORI,XORI immediate versions
LDI, LDIS, LDIF, LDIF2 load typed data immediate
LDTN, STTN load/store typed-data to M(N)
  uses two memory locations
SHFTI shift/adjust exponent
EXTCTI extract field, type-less
  Currently only supports unsigned & signed 16-bit data types
    Sign & magnitude versus 2’s complement under evaluation
    For multiply very little difference in timing or LUT count
    Add, subtract and compare simpler for 2’s complement (no 2nd adder & result mux)
Notes: Residue is register 28 and PC is register 31. N indicates 2’s complement constant, I indicates using D register data type. 24-bit instructions have a full set of indexed or base + offset load/store instructions

## Slide 12: A better implementation TROC16_16hwa
Half Word Aligned, 2nd half word only if needed
16-bit two port memory: addressed location and next location
Still good LUT count
  LUTs LUTram DFF BRAM DSP clock
  16 50 0.5 1 14.9ns
Can continue with this design, adding data types and living with two port register file
  24-bit load/store instructions possible by limiting base register to Residue or PC
Notes: Targeted AMD/Xilinx Vivado 24.2, Spartan-7, Real Digital Boolean Board. Three instruction loop runs, no other test bench.

## Slide 13: Full 16-bit implementation TROC16_16hwatag
Four tag bits added to each register
Half Word Aligned, 2nd half word only if needed
16-bit two port memory: addressed location and next location
LUT count rising, includes signed & unsigned MUL
  Tried area optimization, dramatic improvement in LUT count
  LUTs LUTram DFF BRAM DSP clock
  17 50 0.5 1 14.5ns std flow
  17 50 0.5 1 14.0ns area opt unsigned
  264 17 50 0.5 1 14.1ns 2’s comp +-*?
Notes: Targeted AMD/Xilinx Vivado 24.2, Spartan-7, Real Digital Boolean Board. Three instruction loop runs, no other test bench yet.

## Slide 14: Implementation flow
List of instructions and their formats (spreadsheet)
Op-code allocation (VHDL constants)
  example:
  constant op16_ADD: unsigned(5 downto 0) := "000101"; -- S + D => D
Register file VHDL
Memory block RAM VHDL
Top file was troc16_16min.vhd, troc16_16hwa.vhd
  currently troc16_16hwatag.vhd
  Include constant & op-code files
  Port map Register file & Memory
  Main combinatorial process
  Register update process
Notes: Much of the planning involved refining or reconsidering the instructions and their formats. Necessary instructions, useful instructions

## Slide 15: Troc16_16 block diagram write enables on all registers and both RAMs
state
Residue*
Combinatorial logic
Adders,
MUXes,
Update enables,
Etc.
Output register(s)
LUT RAM
32x20
Dual port
Block RAM
1024x16
Input pins
Memory read data (32 bits)
R value
D value
D in
PC/mem address
Memory write data 16/32 bits
Dadr
Radr
clocked
Write
clock
Read &
Write
clock
PC*
clocked
Notes: *Residue and PC registers MUXed into LUT RAM outputs as per LUT RAM addresses. Modified 2016 diagram.

## Slide 16: Single clock cycle events
Read instruction out of block RAM
Use R & S fields to read operands from LUT RAM
Instruction process uses nested case statements, generates register & memory updates
Set update enables
Update PC, LUT RAM, post address (new PC) to block RAM
Notes: Single cycle implementation much friendlier towards experimentation: can comment code in an out. Generics & conditional generate is the better way.

## Slide 17: Main file (rtoc16_16… .vhd)
use ieee.numeric_std.all;
Component declarations
Variable declarations
Port maps
Mux PC and Residue onto register-file outputs
Main process
Register updates
  Typically three names used:
  name, nameN for next value, nameWE for update enable
Notes: Recommended to use unsigned signals as much as possible with ieee.numeric_std.all Data type coercions via signed, unsigned & std_logic_vector functions.

## Slide 18: Instruction Processing process
Use nest of CASE statements
First set default values for variables
State variable Case (memory load/store, normal)
Op-code size Case (16, 24 & 32-bit instructions)
Op-code Case (32 entries, unsupported instructions commented out)
  Example: when op16_ADD | op16_ADDI => ALUout<=RR + SS; LUTwe<='1'; residueN(0)<= ALUout(16); residuewe<='1';
Data type Case (as necessary, for instance AND, OR & XOR are data type invariant)
Notes: Each instruction updates default values as needed. Loads and store take two clock cycles and thus three states. Will need additional states for interrupts & slow operations.

## Slide 19: Register update RTL
update: process(clk)
begin
if (rising_edge(clk)) then
state<=stateN;
if pcwe = '1' then pc <= pcN; end if;
if residuewe = '1' then residue <= residueN; end if;
if outwe = '1' then out0 <= S; end if;
-- for now only one output port
end if;
end process; -- register & state updates
Register file and memory also have updates using signals from the main process
Notes: VHDL-2008

## Slide 20: Next steps
Formal ISA specification. Precise spec is a must!
Add test bench! Will be a self checking program
Add tag bits to register file: done
Load-immediate for additional data types: done
New data type operators, 2’s complement: done
Limited set of 24-bit instructions
  Constrained by two port register file
Add additional ports to register file
Add byte write enables to memory
24-bit registers and 32-bit memory
  Need assembler to generate memory initialization
Notes: Keeping a log of utilization & Fmax numbers for each variation to evaluate additional instruction’s and optimiation’s performance

## Slide 21: Some day
Implement assembler (not hard)
  Needed to generate memory initialization files
Implement compiler; an example:
  https://www.cs.hiroshima-u.ac.jp/~nakano/wiki/wiki.cgi *
Run benchmarks (there are many, these are shock wave)
  https://www.researchgate.net/publication/323467921 **
  https://helper.ipam.ucla.edu/publications/bdcws2/bdcws2_15049.pdf
Other floats, 16-bit fixed point logarithms
Other word & byte sizes
  There is a way to use ordinary DRAM with 36, 42 & 48-bit word sizes***
Notes: *Nakano uses Flex, Bison & Perl to create gcc compiler. Wirth’s Oberon also a possibility. Problem is register allocation. **Also covers several float formats and their encoding. ***DRAM read/written 256 bits at a time. On read 256 bits split into 7x 36, 6x 42 or 5x 48-bit words with minimal waste.

## Slide 22: Retrospective
Was dragging my feet until considered the subset 16-bit ISA
  Where to start? Minimal implementation, Gratification
AMD/Xilinx Vivado gives advice and better error locations than previously. Linter sometimes helpful.
  Significant LUT count elasticity between area and speed!
Lots of soft-core uPs at www.opencores.org
Or https://github.com/jimbrake/cpu_soft_cores
Used ~same implementation process as in 2016
  Not as concerned with creating temporaries to save LUTs: E.g. Vivado seems to optimize very well
Majority of the time goes into planning / evaluation
An alternative to RISC-V? Requires frozen minimum ISA for tool chain & Linux (no divide, no floats, interrupt support)
Ugh: endless details and variations
Notes: A complete operation code list and their formats helps greatly when doing simplifications/subsetting that will be later supplemented.

## Slide 23: The Residue register
Considered poor design to use status register for zero/carry/overflow signals
Moving these signals to a register file register opens a more general approach
Capturing the upper half multiply and divide remainder solves several problems
Provides a general and efficient approach for multi-word arithmetic
For troc16_16 can provide an implied base or index register for memory load/store without adding a register file port
Notes: IEEE-754 now supports floating-point divide remainder and the residue (round-off portion) of add/subtract/multiply.

## Slide 24: FPGA resources
LUT Lookup table 3 to 6 inputs, 1 to 2 outputs
  Include carry chain for building adders
DFF D flip-flop 1 to 2 per LUT
IO Tristate transceiver with optional DFFs
RAM Variable aspect ratio, usually dual port
  LUT RAM: 16x1, 64x1, 32x2
  Small block RAM: 32x18, 32x20, 64x18
  Block RAM: 128x36 to 1024x36
  Large block RAM: 2Kx72, 4Kx72, 4Kx144
  External DRAM: Built-in controller
Wiring Fabric
  Horizontal and vertical wire segments of various lengths
Notes: From 2016 talk. LUT RAMs typically can have two or more read ports and only one write port.

## Slide 25: LUT + DFF Lattice Semiconductor iCE40FamilyHandbook.pdf pg6-2
Notes: From 2016 talk.

## Slide 26: Input – Output pins Lattice Semiconductor iCE40FamilyHandbook.pdf pg6-7
Notes: From 2016 talk.

## Slide 27: Block RAM Xilinx Spartan-6 FPGA Block RAM Resources User Guide pg12
Notes: From 2016 talk.

## Slide 28: Simplified DSP48A1 slice Xilinx Spartan-6 FPGA DSP48A1 Slice pg 17
Notes: From 2016 talk.

## Slide 29: Wiring Fabric Altera CycloneV Device Handbook pg1-2
Notes: From 2016 talk.

## Slide 30: ROIS24_24uP
    64 24-bit registers: uses 96 LUTs, quad ported
    24 bit instruction with 6-bit op-code and three 6-bit register designators
      XXXXXX DDDDDD RRRRRR SSSSSS (DRS)
      XXXXXX DDDDDD RRRRRR sNNNNN (DRsN)
      XXXXXX DDDDDD sNNNNN NNNNNN (DsNN)
      XXXXXX sNNNNN NNNNNN NNNNNN (sNNN)
    24-bit by 1024 word block RAM main memory
IO ports directly connected to LEDs, Switches, Push button, 100MHz clock
Notes: From 2016 talk. A three data-size, two data-type ISA was defined and never completed.

## Slide 31: rois24_24uP block diagram write enables on all registers and RAMs
PC
state
CCR
Combinatorial logic
Adders,
MUXes,
Update enables,
Etc.
Output register
LUT RAM
64x24
Block RAM
1024x24
Input pins
Memory read data
S value
R value
D value
D in
PC/mem adr
Memory write data
Dadr
Radr
Sadr
clocked
Write
clock
Read &
Write
clock
clocked
Notes: From 2016 talk. For TROC16_16hwa CCR is Residue register, LUTRAM is 32x16 and Block RAM is 1024x16.

## Slide 32: rois24_24uP instruction set
Register zero always reads as zero
XXXXXX DDDDDD RRRRRRR SSSSSSS (DRS)
  Two operands & result registers
  Add, add with carry, subtract, subtract with carry,
  AND, ANDC(2nd operand complemented), OR, XOR
  Call (Jump if D=0; branch to mem[R+S])
XXXXXX DDDDDD RRRRRR sNNNNN (DRsN)
  Sign extended 6-bit immediate combined with R value
  Addi, adci, andi, ori, xori
  Call (Jump if D=0; absolute call/jmp if R=0; return if sN=0)
  In, Out
Notes: From 2016 talk. Big Endian.

## Slide 33: rois24_24uP instruction set cont’d
Load and store: DRS & DRsN
  Load to D, Store from D
XXXXXX DDDDDD sNNNNN NNNNNN (DsNN)
  Conditional branch relative (D is condition code)
  Load immediate
  Call relative
XXXXXX sNNNNN NNNNNN NNNNNN (sNNN)
  Prefix: sNNN will be prefixed to next sN inst
28 instructions currently, room for 64 inst.
Notes: From 2016 talk

## Slide 34: Rois24_24uP minimal program
At 100MHz need more than 24-bits to get blinking lights
Use two registers:
  Add one to first register
  Add carry to second register
  Output second register to LEDs
  Branch back to first instruction
Four instruction loop
  2nd register increments every 0.67 seconds
Notes: From 2016 talk

## Slide 35: Is it working?
Constraint file
  Sets clock speed
  Sets IO pin assignment
  Evaluation kit usually has a sample constraint file
Simulate/debug
  Tools will generate a simple test bench
  Need to relay observed signals out to test bench
  Program acts as the test script
Performance metrics & goals
  Track LUT count and Fmax
Notes: From 2016 talk

## Slide 36: Insights
A deliberate process:
Get something bare bones working
  Minimum instruction set, minimum program
Add instructions
Add to test program
Migrate to block RAM and data-path?*
  Data-path logic is harder to debug
Lots of soft-core uPs at www.opencores.org
Notes: From 2016 talk. *I no longer do data path planning, the tools know best where to place the MUXes and will generate the control signals for you.